## Slide 1
Build/deploy/run VIN Reference App
INVESTIGATION
Date
Name
Position, Department,
Unit
Renesas System Design Co., Ltd.

## Slide 2: AGENDA
Write IPL Page 3
U-Boot Configuration Page 12
Setting Probe Page 16
Booting INTEGRITY Kernel via probe JTAG Page 22
Configure for camera Page 26
Run Vin Reference App Page 30

## Slide 3
1.WRITE IPL

## Slide 4: Data Wirte
File name | Program top address | Flash Save address | Description
bootparam_sa0.srec | 0xE6320000 | 0x000000 | Loader(Boot parameter)
bl2-<board_name>.srec | 0XE6304000 | 0x040000 | Loader
cert_header_sa6.srec | 0xE6320000 | 0x180000 | Loader(Certification)
bl31-<board_name>.srec | 0x44000000 | 0x1C0000 | ARM Trusted Firmware
tee-<board_name>.srec | 0x44100000 | 0x200000 | OP-Tee
u-boot-elf.srec | 0x69000000 | 0x640000 | U-boot

## Slide 5: Download SPI loader and U-boot
Step 1: Connect cable
Step 2: Setting the terminal software
[Setting value] baud rate 115200, 8 bit data, parity none, stop 1 bit ,flow control none

## Slide 6: Download SPI loader and U-boot
Switch Number | Switch Name | Pin 1 | Pin 2 | Pin 3 | Pin 4 | Pin 5 | Pin 6 | Pin 7 | Pin 8
SW1 | QSPI-A | ON | ON | ON | ON | ON | ON | - | -
SW2 | QSPI-B | ON | ON | ON | ON | ON | ON | - | -
SW3 | QSPI-C | OFF |  | - | - | - | - | - | -
SW10 | MODESW-A | ON | ON | ON | ON | ON | OFF | ON | ON
Refer to section 2.2 in RENESAS_RCH3M3_YoctostartupGuide
Step 3: Write data file to HyperFlash
Set dip switch

## Slide 7: Download SPI loader and U-boot
Reset board then start monitor
Set dip switch : SW1, SW2 all OFF; SW3 ON
Execute xls2 command

## Slide 8: Download SPI loader and U-boot
Select HyperFlash.Input “3”.
Input “y”
Input “y”

## Slide 9: Download SPI loader and U-boot
Input Program Top Address & HyperFash Save Address (data write table)
Transmit U-Boot file “file->send file”

## Slide 10: Download SPI loader and U-boot
If there are some data in writing area, "SPI Data Clear(H'FF) Check :H'00000000-0003FFFF Clear OK?(y/n)" is displayed. Then input "y“
Repeat the xls2 command, if other files are written
Power OFF

## Slide 11
Set dip switch to “ Hyper Flash Mode”
Switch Number | Switch Name | Pin 1 | Pin 2 | Pin 3 | Pin 4 | Pin 5 | Pin 6 | Pin 7 | Pin 8
SW1 | QSPI-A | OFF | OFF | OFF | OFF | OFF | OFF | - | -
SW2 | QSPI-B | OFF | OFF | OFF | OFF | OFF | OFF | - | -
SW3 | QSPI-C | ON |  | - | - | - | - | - | -
SW10 | MODESW-A | ON | ON | ON | ON | ON | ON | OFF | OFF
Refer to section 2.2 in RENESAS_RCH3M3_YoctostartupGuide

## Slide 12
2.U-Boot Configuration

## Slide 13
env default -a
setenv bootdelay 1
setenv ipaddr <IP address>
setenv netmask <Netmask address>
setenv gatewayip <Gateway address>
setenv dnsip <Nameserver address>
setenv hostname <hostname>
setenv ethaddr <Ethernet address>
setenv serverip <Server IP address>

## Slide 14
setenv dtbaddr '48000000'
setenv loadaddr '48080000'
setenv imagefile 'hang.bin'
setenv dtbfile r8a7795-es1-salvator-x-multivisor-a57_gen.dtb
setenv bootcmd1 'run setintargs; run bootcmd_kernel_sdcard'
setenv bootcmd_kernel_sdcard 'fatload mmc 0 ${loadaddr} ${imagefile}; fatload mmc 0 ${dtbaddr} ${dtbfile};'
setenv bootcmd2 'fdt addr ${dtbaddr}; fdt resize; fdt chosen; booti ${loadaddr} - ${dtbaddr}'
setenv bootcmd 'run bootcmd1; run bootcmd2'
setenv setintargs 'setenv bootargs device=0 ether=${ethaddr} ipaddr=${ipaddr} netmask=${netmask} gateway=${gatewayip} nameserver=${dnsip} hostname=${hostname}'
save

## Slide 16
3.SETTING FOR PROBE

## Slide 17: Probe firmware setting
Start MULTI (IDE)
Open “Probe Administrator” from “Utilities”.

## Slide 18: Probe firmware setting
File-> NewProbe
Select “Update Firmware” from “Probe”

## Slide 19: Probe firmware setting
Select pbv3_firmware_5.4.4.frm in C:\ghs\T17_0_new\comp_201714\ghprobe and push “Flash Probe” button.
The firmware update will be started.

## Slide 20: Probe configuration setting
Open “command prompt” window from “Start” -> “All programs”.
Set the path to mpadmin.exe ex)> set PATH=%PATH%; C:\ghs\T17_0_new\comp_201714
Change directory that has h3-salvatorx.ghpcfg. Typically, it is C:/GHS/intXXXX/devtree-arm64/rcar ex)> cd C:\ghs\T17_0_new\int1144\devtree-arm64\rcar
Enter the following command. >mpadmin -cfgload -usb rcar-h3.ghpcfg
Ex:

## Slide 21: Probe firmware setting
Select “Configure Probe” from “Probe”.After that select “Configuration” to set clock = 80Mhz, power_detect off

## Slide 22: Note
To run mode partner in IDE, you should request IT to “Configure USB to LAN “
Ex:
serverip 192.168.10.30
ipaddr 192.168.10.100
=>Subnet Mask USB to Lan following 192.168.10.1

## Slide 23
4.Booting INTEGRITY Kernel via Probe JTAG

## Slide 24
1) Configure the R-Car board to load the DTB and boot into the hang image upon power-up or reset, as outlined in the "Board and U-Boot Configuration“ section above.

## Slide 25
2) Configure GHS probe for operation with R-Car board.
3) Connect GHS probe to the R-Car board JTAG port.
4) Build kernel.gpj and open the MULTI debugger on 'kernel'

## Slide 26
5) Connect to the GHS probe using the following connection method:
Green Hills Probe Connection (mpserv) for Renesas Salvator-X
6) Download and execute the kernel. You should observe console output similar to the following:

## Slide 27
5.Configure for camera

## Slide 28: Camera Board Setting
Swicth Number | Pin 1 | Pin 2 | Pin 3 | Pin 4 | Pin 5 | Pin 6 | Pin 7 | Pin 8
SW29 | OFF | OFF | - | - | - | - | - | -
Jumper Number | Pin Number
J9 | 1-2
J17 | 1-2
J18 | 2-3
J19 | 2-3
To connect H3 and Camera Board, refer to “RCARH3_camera_board_setup_guide_20151201” from https://socrm.dgn.renesas.com/repos/s679/trunk/hw/00_Gen3/99_Extended_Camera_Board/

## Slide 29: Build Option
To use camera you have to configure some macro in rivp_vin_root.gpj
macro __PROJECT_APP_CAM=1 # 1 / 4 (camera board only)
macro __PROJECT_APP_INPUT=2 # 0 (HDMI) / 1 (CVBS) / 2 (CameraBoard) / 3 (DPIN)

## Slide 30: Build option
For more information, refer to “Appendix” section in “RIVPV_Reference_Application_03_body.doc”

## Slide 31
6.Run Vin Preference App

## Slide 32
Create “renesas” folder in module folder.
Exact and copy Vin file to renesas folder
Start MULTI (IDE)
Select “Create Workspace” –> “Installed BSPs” -> “Device Tree ARM64” from “Files” of MULTI Launcher window
Device Tree project is created on the MULTI Launcher. Double click “Open Project Manager
Step 2
Step 5

## Slide 33
Add file “rcar_h3_risp.gpj” from “renesas” folder to example.gpj
Click to rivp_vin_root.gpj and build.
Step 5
Step 6

## Slide 34
After building success, click “rivp_vin_monolith.gpj” and debug
Press “Connect” button
Step 7
Step 8

## Slide 35
Click pull-down menu and select “Green Hills Probe Connection (mpserv) for Renesas R-Car H3/M3 on Salvator-X”. If there is no connection setting, you need to open devtree-arm64/default.con by Connection Organizer. Click “Edit” button

## Slide 36
Press “Download” button
After finishing download, click “run” button.
Step 10
Step 11

## Slide 37
Select “Initial” and press “Go on selected items”

## Slide 38
Renesas.com